# NAFSTR: Networked Automated Fingerprint Scanner Test Robot
Jacob Glueck

### NAFSTR uses fingerprint spoofs and four independent fingers to test fingerprint scanners.
Illustration 1: Labeled front view of NAFSTR.	Illustration 2: Photograph of NAFSTR with fingerprint scanner.	Illustration 3: Labeled exploded view of NAFSTR's parts.

#### Features
- Four independently actuated fingers.
- Interchangeable fingerprints.
- Can detect when the scanner has captured a fingerprint.
- Can monitor force being applied to each finger.
- Controllable through a serial connection over USB, through a TCP connection over Ethernet, and through a UDP connection over Ethernet.
- Controllable over Telnet.
- Can move each finger to a specified position or until the scanner captures a fingerprint.
#### Construction
All parts were 3D printed.
#### Fingerprint Spoofs
- 3D Printed:
  - Simple arrangement of thick lines and curves 3D printed in MakerBot Flexible Filament.
  - 0.4 mm thick 3D printed fingerprint mounted to 8 mm thick foam.
    Illustration 4: Labeled view of finger and fingerprint.
- Gelatin
  - Made by pouring gelatin and graphite into a fingerprint mold.
#### Uses
- Stress testing for Web Services-Biometric Devices (WS-BD).
  - WS-BD is a standard for communication with biometric devices using web services.
  - The robot could operate for days and put thousands of finger combinations down onto the scanner.
- Analyzing spoof detection methods
  - The robot can place fingerprint spoofs with a consistent position and consistent, selectable force onto fingerprint scanners. This process could be repeated for hours with different forces and fingerprints to determine how well spoof detection methods work.
#### Finger Motion and Sensors
- Each finger is connected to a servo motor which can provide about 0.8 N·m of torque.
- Each fake fingerprint is mounted onto a fingerprint holder.
- Sandwiched between the holder and the fake fingerprint is a Force Sensitive Resistor (FSR).
- The fingerprint scanner has 4 lights which turn green when the fingerprint has been read. The robot uses 4 Light Dependent Resistors (LDRs), one for each light on the fingerprint scanner, to determine when the lights turn green.
  Illustration 5: Labeled top view of scanner and NAFSTR.